## Slide 1: Multimedia Technieken
Raspberry Pi Standard Boot Process

## Slide 2: Storage
Typically an embedded system has onboard non-volatile memory to store the bootloader and/or kernel images
To cut cost the Raspberry Pi developers decided to omit this
All boot loader code, kernel images and file systems are to be stored on an SD card
The boot loader binaries and kernel images are stored on the first partition of the SD card
  FAT32 or FAT16
If the root filesystem is non-volatile then it can be stored on a second partition
  In our case we use an ext4 filesystem

## Slide 3: Raspberry Pi Boot Process
The Raspberry Pi’s Broadcom BCM2835 system on a chip (SoC) powers up with its ARM1176JZF-S 700 MHz processor held in reset.
The VideoCore IV GPU core is responsible for booting the system.
It loads the first stage bootloader from a ROM embedded within the SoC.
The first stage bootloader is designed to load the second stage bootloader (bootcode.bin) from a FAT32 or FAT16 filesystem on the SD Card.
The second stage bootloader - bootcode.bin - is executed on the VideoCore GPU and loads the third stage bootloader - start.elf.
Historically, yet another bootloader called loader.bin was loaded at this stage, but has since been phased out

## Slide 4: Raspberry Pi Boot Process
So basically
First Stage Bootloader
[SoC ROM]
Second Stage Bootloader
[bootcode.bin]
Third Stage Bootloader
[start.elf]
These can actually be replaced by other bootloaders such as U-Boot

## Slide 5: Raspberry Pi Boot Process
The third stage bootloader - start.elf - is where all the action happens.
It reads config.txt
  a text file containing configuration parameters for
    the VideoCore
      Video/HDMI modes
      memory
      console frame buffers
      etc
    and the Linux kernel
      load addresses
      device tree
      uart/console baud rates
      etc.

## Slide 6: Raspberry Pi Boot Process
Once the config.txt file has been loaded and parsed, the third stage bootloader will also loads cmdline.txt and kernel.img.
  cmdline.txt is a file containing the kernel command line parameters to be passed to the kernel at boot.
  It will load kernel.img into the shared memory allocated to the ARM processor, and release the ARM processor from reset.
The third stage bootloader - start.elf, also passes extra parameters to the kernel than contained within the cmdline.txt.
Your kernel should now start booting.