## Slide 1: Multimedia Technieken 2015 – 2016
Raspberry Pi 2 - Minibian

## Slide 2: Setting up an Embedded System
To setup an embedded Linux system we have multiple choices:
  Use a pre-built binary distribution such as Raspbian, Ubuntu or Fedora
    Quick to set up, but not very flexible: support for only a few architectures, no flexibility on package configuration, no easy way to rebuild the entire system automatically.
  Build all system components manually
    Highly flexible, but painful and inefficient: need to handle complex cross-compilation issues, understand inter-package dependencies, not reproducible.
  Use an automated build system, that builds the entire system from source
    Automated, flexible, handle most cross-compilation issues
    Examples: Buildroot, OpenWRT, PTXdist, OpenBricks, OpenEmbedded, Yocto, etc.

## Slide 3: Using a Minimal Image
For the sake of simplicity we start by using a pre-build image
  Raspbian is a very good choice
    Easy to setup
    Debian based so familiar
  Problem is classroom
    Image read and write take too long
      Too big
    Solution
      Minibian

## Slide 4: Minibian
Minimal Raspbian-based Linux image for Raspberry Pi.
Main Focus
  Small, updated and stable distribution that is fully compatible with official Raspbian “wheezy” image, without GUI and unneeded tools.
Perfect for embedded projects
Very small footprint, boots in some seconds and uses just few of precious RPi RAM.
MINIBIAN has not been obtained purging unneeded packages from original image, neither recompiling the source code
  It’s just a customized Raspbian installation obtained from the same repository used for official RPi wheezy image.
  So kernel and binary files are exactely the same you will find on standard image, with the difference that MINIBIAN fit on 512MB SD Card, is fastest, and updated more often.

## Slide 5: Raspberry Pi 2 - Minibian
Booting Minibian

## Slide 6: Downloading the Image
Minibian can be downloaded here
  https://minibianpi.wordpress.com/
You will need a program like 7zip to extract the tarball

## Slide 7: Creating an SD card - Windows
Next the IMG file can be written to an SD card of at least 1GB using Win32 Disk Imager
  Select the image file and the correct device
  Next hit the write button
To make a backup later on just select a non-existing image file (choose location and name yourself)
  Select the correct device
  Hit the read button

## Slide 8: Creating an SD card - Linux
Just use the ‘dd’ command to write the image to the SD card
  This is not possible from a virtual machine
    No direct (RAW) access to SD Card on host machine
bioboost@NDWMINT ~ $ sudo dd if=<image> of=/dev/mmcblk0 bs=1M

## Slide 9: Success
Insert the SD card into the Pi and connect the power supply
  This perfectly boots.
  Attaching a serial to USB would show you the kernel message
However the actual login prompt is not displayed
  It is actually available through HDMI

## Slide 10: Raspberry Pi 2 - Minibian
Connecting Remotely to the Raspberry Pi

## Slide 11: Connecting Remotely to a Linux System
There are a couple of ways that you can access a shell (command line) remotely on most Linux/Unix systems.
One of the older ways is to use the telnet program, which is available on most network capable operating systems.
  Poses a danger in that everything that you send or receive over that telnet session is visible in plain text on your local network, and the local network of the machine you are connecting to.
  So anyone who can "sniff" the connection in-between can see your username, password, email that you read, and commands that you run.
  For these reasons you need a more sophisticated program than telnet to connect to a remote host.

## Slide 12: Secure SHell
SSH (Secure Shell), was designed and created to provide the best security when accessing another computer remotely.
Not only does it encrypt the session, it also provides better authentication facilities, as well as features like
  secure file transfer,
  X session forwarding
  port forwarding
  …
It can use different forms of encryption ranging anywhere from 512 bit on up to as high as 32768 bits and includes ciphers like AES (Advanced Encryption Scheme), Triple DES, Blowfish, CAST128 or Arcfour.
  Of course, the higher the bits, the longer it will take to generate and use keys as well as the longer it will take to pass data over the connection.

## Slide 13: Telnet
Telnet
  Unsecure
SSH
  Secure

## Slide 14: Connect to Raspberry Pi
You can use the ‘ssh” command
Or you can use the putty tool
  To use putty first install it using apt-get
bioboost@NDWMINT ~ $ sudo apt-get install putty
bioboost@NDWMINT ~ $ ssh <username>@<ip-address>

## Slide 15: Connect to Raspberry Pi
We do however still need the IP address of the Pi
  Use windows netscan or use the ‘nmap’ tool on linux
bioboost@NDWMINT ~ $ nmap –sn <network>/<mask_size>
Starting Nmap 6.00 ( http://nmap.org ) at 2015-09-27 13:10 BST
Nmap scan report for 10.0.0.2
Host is up (0.00064s latency).
MAC Address: D4:BE:D9:5E:38:FF (Dell)
Nmap scan report for 10.0.0.3
MAC Address: B8:27:EB:DD:96:A1 (Raspberry Pi foundation)
Nmap scan report for 10.0.0.5
Host is up (0.00078s latency).
MAC Address: 00:22:68:64:37:60 (Hon Hai Precision Ind. Co.)
Nmap scan report for 10.0.0.64
Host is up (0.00040s latency).
MAC Address: 18:59:33:14:51:47 (Cisco Spvtg)
...
Nmap done: 256 IP addresses (5 hosts up) scanned in 3.06 seconds

## Slide 16: Connect to Raspberry Pi
So once we know the IP address we can connect to the Pi
  Default username of Minibian: root
  Default password of Minibian: raspberry
bioboost@NDWMINT ~ $ ssh root@<ip_address>
login as: root
root@<ip_address>'s password:
Linux raspberrypi 3.18.7-v7+ #755 SMP PREEMPT Thu Feb 12 17:20:48 GMT 2015 armv7l
The programs included with the Debian GNU/Linux system are free software;
the exact distribution terms for each program are described in the
individual files in /usr/share/doc/*/copyright.
Debian GNU/Linux comes with ABSOLUTELY NO WARRANTY, to the extent
permitted by applicable law.
Last login: Sun Sep 27 13:04:01 2015 from 10.0.0.5
root@raspberrypi:~#

## Slide 17: Raspberry Pi 2 - Minibian
Manually resizing the SD card on the Raspberry Pi

## Slide 18: Manually resizing the SD card on the Raspberry Pi
You can actually resize the partitions of the SD card that your Pi is running on
First you need to change the partition table with fdisk.
You need to remove the existing partition entry and create a new one
  This will only change the partition table, not the partitions data on disk.
  The start of the new partition needs to be aligned with the old partition!
Then delete partitions with d and create a new with n.
You can view the existing table with p.
root@raspberrypi:~# fdisk /dev/mmcblk0

## Slide 19: Manually resizing the SD card on the Raspberry Pi
p to see the current start of the main partition
  d, 2 to delete the main partition
  n p 2 to create a new primary partition
    next you need to enter the start of the old main partition and then the size.
    The main partition on the Minibian image from 2015-02-18 starts at 97728
      But the start of your partition might be different. Check the p output!
w write the new partition table

## Slide 20: Manually resizing the SD card on the Raspberry Pi
root@raspberrypi:~# fdisk /dev/mmcblk0
Command (m for help): p
Disk /dev/mmcblk0: 7969 MB, 7969177600 bytes
4 heads, 16 sectors/track, 243200 cylinders, total 15564800 sectors
Units = sectors of 1 * 512 = 512 bytes
Sector size (logical/physical): 512 bytes / 512 bytes
I/O size (minimum/optimal): 512 bytes / 512 bytes
Disk identifier: 0x0004a452
Device Boot Start End Blocks Id System
/dev/mmcblk0p1 16 97727 48856 b W95 FAT32
/dev/mmcblk0p2 97728 999423 450848 83 Linux

## Slide 21: Manually resizing the SD card on the Raspberry Pi
Command (m for help): d
Partition number (1-4): 2
Command (m for help): n
Partition type:
p primary (1 primary, 0 extended, 3 free)
e extended
Select (default p): p
Partition number (1-4, default 2): 2
First sector (97728-15564799, default 97728):
Using default value 97728
Last sector, +sectors or +size{K,M,G} (97728-15564799, default 15564799): +750M
Command (m for help): w
The partition table has been altered!
Calling ioctl() to re-read partition table.
WARNING: Re-reading the partition table failed with error 16: Device or resource busy.
The kernel still uses the old table. The new table will be used at
the next reboot or after you run partprobe(8) or kpartx(8)
Syncing disks.

## Slide 22: Manually resizing the SD card on the Raspberry Pi
Next just restart the Raspberry Pi
After the reboot you need to resize the filesystem on the partition.
  The ‘resize2fs’ command will resize your filesystem to the new size from the changed partition table.
root@raspberrypi:~# reboot
root@raspberrypi:~# resize2fs /dev/mmcblk0p2
resize2fs 1.42.5 (29-Jul-2012)
Filesystem at /dev/mmcblk0p2 is mounted on /; on-line resizing required
old_desc_blocks = 2, new_desc_blocks = 3
The filesystem on /dev/mmcblk0p2 is now 768000 blocks long.

## Slide 23: Manually resizing the SD card on the Raspberry Pi
You can check the new available space using the disk-free command
root@raspberrypi:~# df –h
Filesystem Size Used Avail Use% Mounted on
rootfs 719M 334M 347M 50% /
/dev/root 719M 334M 347M 50% /
devtmpfs 484M 0 484M 0% /dev
tmpfs 98M 188K 98M 1% /run
tmpfs 5.0M 0 5.0M 0% /run/lock
tmpfs 195M 0 195M 0% /run/shm
/dev/mmcblk0p1 48M 15M 34M 30% /boot
tmpfs 195M 0 195M 0% /tmp