## Slide 1: Multimedia Technieken
Buildroot

## Slide 2: Building Embedded Linux Systems
To create an embedded Linux system we have multiple choices:
  Use a pre-built binary distribution such as Debian, Ubuntu or Fedora
    Quick to set up, but not very flexible: support for only a few architectures, no flexibility on package configuration, no easy way to rebuild the entire system automatically.
Build all system components manually
  Highly flexible, but painful and inefficient: need to handle complex cross-compilation issues, understand inter-package dependencies, not reproducible.
Use an automated build system, that builds the entire system from source
  Automated, flexible, handle most cross-compilation issues
  Examples: Buildroot, OpenWRT, PTXdist, OpenBricks, OpenEmbedded, Yocto, etc.

## Slide 3: Buildroot Main Characteristics
Based on well-known technologies:
  kconfig for the configuration interface and language
  make for the build logic
  These technologies are familiar to all embedded Linux developers.
Very simple to use, and easily hackable code base. The core infrastructure is a few hundred lines of make code.
Fast. It does really build only what’s necessary. The base system, composed only of BusyBox, takes less than 3 minutes to build with an external toolchain.
Designed for small to medium sized embedded systems. There is no runtime package management system (dpkg, rpm). Complete rebuilds are often required. Well-suited for systems with a limited number of components.

## Slide 4: General Principle

## Slide 5: Buildroot
Getting the Latest Buildroot

## Slide 6: Getting the Latest Buildroot
Latest stable release:
  Download the latest tar-bal from http://buildroot.uclibc.org/download.html
Latest development repository
$ tar -xvzf buildroot-2014.08.tar.gz
# x indicates an extraction
# v gives extra output (verbose)
# z is for a gz compressed archive
# f is a file specifier
git clone git://git.buildroot.net/buildroot

## Slide 7: Buildroot
Building it all

## Slide 8: Host System Requirements
Your host system will need some libraries, tools and packages before we can use Buildroot
Buildroot will generate errors when dependencies are not met
  Luckily you can always continue the build process after installing missing dependencies
Following packages are mandatory
$ sudo apt-get install git git-core libncurses5 libncurses5-dev build-essential

## Slide 9: Buildroot and Raspberry Pi
Buildroot comes with predefined configuration files for many popular embedded systems
Check out buildroot/config/ directory for available configurations
Select configuration using the make command as followed
Creates a configuration file in buildroot/ with the name .config
$ make raspberrypi_defconfig

## Slide 10: Building it all
Once the configuration is defined and saved in .config, the compilation process is started by using the make command
  This will take a while the first time
  Buildroot will automatically download, extract, patch, configure, compile and install the selected components, taking care of the necessary dependencies.
  Never run this as root ! (no need)
  Very limited set of dependencies:
    a native compiler, and basic utilities like awk, bison, patch, gzip, tar, wget, etc.
$ make

## Slide 11: Building it all - Result
Check buildroot/output/images for the generated files for your target system
  rootfs.tar
    This is your rout filesystem. It still needs to be extracted to its own partition on an SD card
  rpi-firmware (bootcode.bin, cmdline.txt, config.txt, fixup.dat, startup.elf)
    These are the bootloaders and configuration files for booting your Pi
  zImage
    The kernel image
├── rootfs.tar
├── rpi-firmware
│ ├── bootcode.bin
│ ├── cmdline.txt
│ ├── config.txt
│ ├── fixup.dat
│ └── start.elf
└── zImage

## Slide 12: Buildroot
Booting the Raspberry Pi

## Slide 13: Preparing the SD card
Instructions can be found under board/raspberrypi/readme.txt
It states that we need two partitions
  FAT32 boot partition
  EXT3 / EXT4 root filesystem partition
At the root of the boot partition, the RaspberryPi must find the following files:
  bootcode.bin
  config.txt
  fixup.dat
  start.elf
  zImage
The kernel image file name is defined in config.txt like “kernel=zImage”.
  Can be changed if you wish
$ cat buildroot/board/raspberrypi/readme.txt

## Slide 14: Preparing the SD card
Would be really easy when we had RAW access to SD card from virtual machine
Solution:
  Creating our own image file and use Win32 Disk Imager to write the image to the SD card

## Slide 15: Preparing the SD card – Solution outline
Create an image file (50MB)
Create both partitions using the fdisk tool
$ cd ~
$ dd if=/dev/zero of=minimal_pi.img bs=1M count=50
$ fdisk minimal_pi.img
Disk minimal_pi.img: 52 MB, 52428800 bytes
255 heads, 63 sectors/track, 6 cylinders, total 102400 sectors
Units = sectors of 1 * 512 = 512 bytes
Sector size (logical/physical): 512 bytes / 512 bytes
I/O size (minimum/optimal): 512 bytes / 512 bytes
Disk identifier: 0xef02b601
Device Boot Start End Blocks Id System
minimal_pi.img1 2048 22527 10240 4 FAT16 <32M
minimal_pi.img2 22528 102399 39936 83 Linux

## Slide 16: Preparing the SD card – Solution outline
Use the kpartx tool to map both paritions to a loop device
  A loop device allows us to access a file as a block device (example of a block device is HDD)
  Both partitions can now be accessed via
    /dev/mapper/loop0p1
    /dev/mapper/loop0p2
Now the partitions can be formatted with a filesystem
$ kpartx –a minimal_pi.img
$ sudo mkfs.vfat -F 16 -n boot /dev/mapper/loop0p1
$ sudo mkfs.ext4 -L rootfs /dev/mapper/loop0p2

## Slide 17: Preparing the SD card – Solution outline
Next we mount the newly formatted partitions so we can add the necessary files to them
Copy the files to the partitions
$ sudo mkdir -p /mnt/boot
$ sudo mkdir -p /mnt/rootfs
$ sudo mount -o rw,sync /dev/mapper/loop0p1 /mnt/boot
$ sudo mount -o rw,sync /dev/mapper/loop0p2 /mnt/rootfs
$ sudo cp buildroot/output/images/zImage /mnt/boot
$ sudo cp buildroot/output/images/rpi-firmware/* /mnt/boot
$ sudo tar -xpsf buildroot/output/images/rootfs.tar -C /mnt/rootfs

## Slide 18: Preparing the SD card – Solution outline
The cmdline.txt also need to be changed a bit. Open it using nano:
Make sure the content reads:
Unmount both partitions and detach the loop device with kpartx
  Also copy the image to your share
$ sudo nano /mnt/boot/cmdline.txt
dwc_otg.fiq_fix_enable=1 sdhci-bcm2708.sync_after_dma=0 dwc_otg.lpm_enable=0 console=ttyAMA0,115200 root=/dev/mmcblk0p2 rootfstype=ext4 rootwait
$ sudo umount /mnt/boot
$ sudo umount /mnt/rootfs
$ sudo kpartx –d minimal_pi.img
$ cp minimal_pi.img /media/sf_VMShare

## Slide 19: Preparing the SD card - Automated
All these steps have been automated using a shell script called ‘sdcard.sh’. Copy it to your homedir and make sure it is executable
Change the location of buildroot inside the script using nano
Run the script
$ sudo chmod +x sdcard.sh
$ nano sdcard.sh
$ cd ~
$ ./sdcard.sh

## Slide 20: Success
This perfectly boots.
Attaching a serial to USB would show you the kernel message
However the actual login prompt is not displayed
  It is actually available through HDMI

## Slide 21: Buildroot
Configuring your system

## Slide 22: Needs more configuration
Some things we still need to configure
  Custom root file system
  Setup the network interface
  Remote access via SSH
  Spawning a getty on the serial line

## Slide 23: Custom Root File System
Before we can continue we will need a way to add our own files to the file system and make changes to existing files
Buildroot implements a simple way of doing this
  The first step is to create the following directory structure inside your home folder
  “Config.in” and “external.mk” are empty files that are mandatory
$ tree pi_buildroot_custom/
pi_buildroot_custom/
├── board
│ └── raspberrypi
│ └── rootfs_overlay
├── Config.in
└── external.mk
3 directories, 2 files

## Slide 24: Custom Root File System
  Next we need to tell Buildroot where this directory can be found
    This only needs to be done once !
    Make sure to specify the absolute path of your customizations directory
    This is automatically saved in “output/.br-external”
$ make BR2_EXTERNAL=/home/nico/pi_buildroot_custom

## Slide 25: Custom Root File System
  Now we need to tell Buildroot to use “/home/nico/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/” as a root filesystem overlay
    Issue
    Navigate to
    and change “Root filesystem overlay directories” to
    Save and exit
$ make menuconfig
System configuration
$(BR2_EXTERNAL)/board/raspberrypi/rootfs_overlay

## Slide 26: Custom Root File System
Just create a new file called info in “/home/nico/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/”
  Just add some text identifying this as being your system
$ nano /home/nico/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/info

## Slide 27: Setup the network interface
For the moment all we need to do is activate the network interface.
We just added our own filesystem overlay so this is easy
Create a file called “interfaces” in “etc/network”
And copy the following content to the file
$ cd ~/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/
$ mkdir –p etc/network
$ cd etc/network
$ touch interfaces
auto lo
iface lo inet loopback
auto eth0
iface eth0 inet dhcp

## Slide 28: Setup the network interface
Apparently sometimes it happens that the network controller is not yet operational and Linux already tries to bring up the interface
  In this the network interfaces never comes up and the interface also receives no IP address
To fix this we need to add a delay to the script that brings up the network interfaces
  The script that brings up the interfaces can be found at “/buildroot/output/target/etc/init.d/S40network”
  We can copy this to our root file system overlay and modify it
$ mkdir –p ~/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/etc/init.d
$ cp –a ~/buildroot/output/target/etc/init.d/S40network ~/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/etc/init.d/

## Slide 29: Setup the network interface
Next we need to add a “sleep 2” before the “ifup” command
With the end result being
$ cd ~/pi_buildroot_custom/board/raspberrypi/rootfs_overlay/etc/init.d/
$ nano S40network
#!/bin/sh
#
# Start the network....
#
case "$1" in
start)
echo "Starting network..."
sleep 2
/sbin/ifup -a
;;
stop)
echo -n "Stopping network..."
/sbin/ifdown -a
;;
restart|reload)
"$0" stop
"$0" start
;;
*)
echo "Usage: $0 {start|stop|restart}"
exit 1
esac
exit $?

## Slide 30: Adding an SSH daemon
First of all we need to configure the system with an SSH daemon so we can login remotely
  The perfect candidate for this is dropbear which can be retrieved from https://matt.ucc.asn.au/dropbear/dropbear.html
  However since this is a requirement almost every embedded system needs it was added to Buildroot
To configure Buildroot to add the dropbear ssh daemon start the buildroot menu config
  This allows you to configure the overall Buildroot system
$ cd ~/buildroot
$ make menuconfig

## Slide 31: Adding an SSH daemon
Navigate to
and check
How could you ever have found this yourself ?
  Google
  menuconfig + search (/)
Target packages => Networking applications
dropbear

## Slide 32: Adding an SSH daemon
Dropbear will not allow a user to login with a user account which does not have a password
  The root account does not have a password default
Navigate to
and set a “Root password”
System Configuration

## Slide 33: Adding an SSH daemon
Save the configuration and issue a make command
Execute the sdcard.sh shell script
Write the image to the SD card and reboot the Pi
$ make
$ ~/sdcard.sh

## Slide 34: Spawning a getty on the serial line
To spawn a console to the serial line (necessary for debugging) you need to configure Buildroot
Navigate to
and change the “TTY port” to
which is the name of the serial port on the Raspberry Pi
$ make menuconfig
System configuration => Run a getty (login prompt) after => getty options
ttyAMA0

## Slide 35: Problems ?
Step 1: Keep calm
Step 2: Retrace your steps and make sure you did not mess anything up
Step 3: Panic
Step 4: Ask for a Serial to USB converter and debug

## Slide 36: Buildroot
Room for improvements

## Slide 37: System in Development
Is this a manageable setup for a system in development ?
  Real world development setup would for example use a boot loader which could fetch the kernel and root file system from a network drive
    This would allow you to omit the SD card write step
    Much faster for testing
    More complex to setup
    Requires a working network interface